RESEARCH-RELATED EXPOSURE TO NONIONIZING RADIATION

1.	STUDY TITLE

2.	PRINCIPAL/OVERALL INVESTIGATOR

3. MAGNETIC RESONANCE IMAGING

| Manufacturer and Model: Siemens Allegra (or Trio) 3T Scanner |
| --- |
| Are the exposure parameters routine? | YES | NO | If NO, complete below |
| Is contrast being used? YES NO |
| Static Magnetic Field Strength (Gauss): 30,000 |
| SAR/Average and Peak RF Heating: SAR: 3W/kg, Heat<1degC |
| Rate of Magnetic Field Strength Change with Time (dB/dt) Relative to Gradient: < 20T/s for TC 120us |
| Acoustic Noise (decibels): <98dBA (with mandatory hearing protection) |
| Part of Body Exposed: head | Duration of Exposure: ~2 hours |
| Discuss why these parameters are being used: standard brain fMRI parameters used |

4. ULTRASOUND

| Manufacturer and Model: |
| --- |
| Are the exposure parameters routine? | YES | NO | If NO, complete below |
| Is contrast being used? YES NO |
| Frequency (Hz) and Intensity (W/cm2): |
| Part of Body Exposed: | Duration of Exposure: |
| Discuss why these parameters are being used: |

5. LASERS OR ULTRAVIOLET RADIATION

| Manufacturer and Model: |
| --- |
| Are the exposure parameters routine? | YES | NO | If NO, complete below |
| Power Output (W/cm2)/Wavelength (nm)/Tissue Exposure (J/cm2): |
| Part of Body Exposed: | Duration of Exposure: |
| Discuss why these parameters are being used: |
| Identify individuals responsible for operating laser: |
| Note: Laser operators must complete institutional training and credentialing process. Submit documentation of laser training and credentialing with protocol. |

FOR ASSISTANCE CONTACT:	BWH:  Director, Health Physics Office at (617) 732-6057

DFCI:  Environmental Health and Safety at (617) 632-3005

MGH:  Radiological Sciences at (617) 726-8326

FOR LASER TRAINING:	BWH:  Pat Baptiste at (617) 732-8314

MGH:  Beverly Dammin at (617) 726-3308