## Slide 1: Improvements in SlicerRT, the radiation therapy research toolkit for 3D Slicer
Csaba Pinter1, Andras Lasso1, An Wang2, David Jaffray2, and Gabor Fichtinger1
1Laboratory for Percutaneous Surgery, Queen’s University, Canada 2University Health Network, Toronto, ON, Canada

## Slide 2: Motivation behind SlicerRT
Commercial treatment planning systems (TPS)
Existing research tools CERR, PLUNC, dicompyler, etc.
Expensive
Closed
Cover only routine clinical procedures
Stable
Unstable
User-friendly
Not extensible
Not flexible
Poor documentation
Large, non-modular code base
Insufficient user and developer support
Inconvenient
Well documented
Limited feature set
Flexible
Extensible
SlicerRT
Open-source
Platform-independent
Open-source?
Free
Notes: Lack of a comprehensive and open radiation therapy toolkit
RT researchers use commercial TPSs along with existing research tools. Both categories have serious shortcomings when being used for research purposes.
.. aspires to overcome these limitations, and also congregate their strong properties, such as …

## Slide 3
DICOM-RT import/export
Import integrated into core DICOM import plugin mechanism
Supported data types:
  RT structure sets → Contours → Fiducial point
  RT dose map
  RT image
  RT plan isocenter, beams
  Planning CT, MR, etc.
Basic DICOM-RT export is implemented
Standard layout after loading phantom dataset
Notes: - … main feature groups of SlicerRT
- The first step of every RT research workflow … broad spectrum of data … seamless handling and loading of the data using only the DICOM browser in 3D Slicer.
- export

## Slide 4
Contour analysis
Multiple representations (automatic conversion)
  Ribbon model
  Rasterized volume
  Closed surface model
Contour comparison
  Dice coefficient
  Hausdorff distance
Contour morphology
  Expand, shrink
  Combine using logical operators
Rasterized volume
Ribbon model
Closed surface
Notes: easy handling of the imported structure set contours, by offering multiple representations and automatic conversions between those. The supported representations are…
Improving this feature is one of our main focus: rasterize, closed surface

## Slide 5
Dose volume histogram
Dose analysis
Dose volume histogram (plot visualization + metrics)
Dose accumulation
Dose comparison (gamma)
Isodose contours / surfaces
External beam planning (photon, proton)
Registration
  BSpline registration
  Landwarp registration
Gamma dose comparison
Isodose contours and surfaces

## Slide 6
External beam planning
This module provide basic framework for RT planning and dose calculation for photon and proton
Photon MLC beam created in external beam planning module
Notes: This module provide basic framework for RT planning and dose calculation.
1. Visualize RT plan, loaded or created. 1A. QA purposes 1B. IMRT optimization (once they have a nice dose matrix, they want to show the beams overlaid with the dose)
2. Dose calculation

## Slide 7
External beam planning - proton
Aperture
Range compensator
Target
Beam dose distribution
External beam planning module UI
Notes: Spherical target at the center of a cylinder.
Choose target in UI -> Aperture, conform to the target
Range compensator: black=thin, gray=thicker

## Slide 8
Subject hierarchy
New concept for organizing data
Nice and intuitive way of organizing and handling data Bring basic features in a data-centered tree view, such as
  Show/hide
  Transform branch
Extendable through plugins Broad API allowing many customizations, such as
  DICOM export
  Registration
Subject hierarchy module widget
Notes: Our other current focus of research and development is data management …
many nice RT-related features, overviewing the loaded data inconvenient … familiar to TPS and eval. ws.

## Slide 9
Subject hierarchy - plugins
Default
DICOM
Volumes
Registration
Parse local data
Contours
RT objects
Many more to come …
ParseLocalData plugin in action
Notes: - Wide range of problems to solve here
- Most plugins provide a role that the data nodes can assume, for example … other plugins provide only context menu actions (PLD)
- Generally, these plugins provide the tree processing functionality to allow a more data-centric usage of Slicer instead of the operation and module centric approach … please keep this in mind when you use this module, and need only one or two small features to make your workflow more easy to perform

## Slide 10
Non-linear transform support
Transforms are applicable in “real-time” to
  Volumes (slice views, slice view in 3D)
  Models (3D view, slice intersection)
  Markup points, ruler
Transform types
  Linear
  B-spline: arbitrary grid orientation, optional bulk transform
  Grid (displacement field): arbitrary grid orientation
Operations
  Display
  Invert
  Combine
Limitations
  Volume rendering, processing in CLI modules: not real-time, need to harden transform
  Composite transform cannot be saved
  Annotation ROI transform is limited
  Not possible to define a “reference” volume when hardening a transform
Notes: - Wide range of problems to solve here
- Most plugins provide a role that the data nodes can assume, for example … other plugins provide only context menu actions (PLD)
- Generally, these plugins provide the tree processing functionality to allow a more data-centric usage of Slicer instead of the operation and module centric approach … please keep this in mind when you use this module, and need only one or two small features to make your workflow more easy to perform

## Slide 11
Transform info
Notes: - Wide range of problems to solve here
- Most plugins provide a role that the data nodes can assume, for example … other plugins provide only context menu actions (PLD)
- Generally, these plugins provide the tree processing functionality to allow a more data-centric usage of Slicer instead of the operation and module centric approach … please keep this in mind when you use this module, and need only one or two small features to make your workflow more easy to perform

## Slide 12
Transform display
Notes: - Wide range of problems to solve here
- Most plugins provide a role that the data nodes can assume, for example … other plugins provide only context menu actions (PLD)
- Generally, these plugins provide the tree processing functionality to allow a more data-centric usage of Slicer instead of the operation and module centric approach … please keep this in mind when you use this module, and need only one or two small features to make your workflow more easy to perform

## Slide 13
Transform display
Notes: - Wide range of problems to solve here
- Most plugins provide a role that the data nodes can assume, for example … other plugins provide only context menu actions (PLD)
- Generally, these plugins provide the tree processing functionality to allow a more data-centric usage of Slicer instead of the operation and module centric approach … please keep this in mind when you use this module, and need only one or two small features to make your workflow more easy to perform

## Slide 14
Gel dosimetry analysis
“Slicelet” for gel dosimetry analysis workflow
Wizard-like simplified user interface
Notes: - basically a Slicer module that includes a full layout, and can be run separately from the main Slicer window, thus allowing a simplified, workflow-based interface, so that the user can focus on the task at hand.
- Gel dosimetry … used in commissioning new radiation techniques and comparison of planned and delivered dosage, among other things
- wizard-like

## Slide 15
Collection of RT-specific modules, includes
Distributed as a 3D Slicer extension: can be downloaded, installed, upgraded using the extension manager in Slicer
SlicerRT extension for 3D Slicer
SlicerRT extension in the 3D Slicer app store (free)
Notes: SlicerRT is distributed as a 3D Slicer extension. It can be easily found and installed from the Slicer Extension Manager.

## Slide 16
Next steps
Planned for the next 6 months:
DICOM-RT export
External beam planning
Contour mechanism – integration to 3D Slicer core
Digitally reconstructed radiograph (DRR)
Rasterization evaluation and improvements
Scripting examples
More testing and validation
More information: http://SlicerRT.org
Notes: Suggestions, comments and feature requests are warmly welcome! Our weekly meetings every Wednesday are also open to anybody to discuss any matter related to the toolkit.

## Slide 17
Thank you for your attention!