## Slide 1: DTI Atlas Registration via 3D Slicer and DTI-Reg
Martin Styner, UNC
Clement Vachet, UNC
Jean-Baptiste Berger, UNC

## Slide 2: DTI Registration
This tutorial teaches you how
  What fiber tract analysis is
  How to perform a fiber tract measurements via DTIAtlasFiberAnalyzer in Slicer
DTIAtlasFiberAnalyzer
  On NITRC, works also as standalone
  Works on population/groups of datasets

## Slide 3: Dataset
For this tutorial you will need DTI and fiber data files that can be found on this link : http://hdl.handle.net/1926/1759

## Slide 4: Needed Ingredients
A DTI atlas with fiber tracts
  Create your own atlas
    Track in Slicer, process with FiberViewerLight
      Separate Tutorial
    Atlas building in Slicer in progress
DTI datasets mapped into the atlas
  Directly mapped DTI data
  DTI & Deformation field data

## Slide 5: Let’s get started: Slicer 4
Linux/Mac users :
Launch the Slicer
executable located in
the Slicer4 directory
Windows users :
Select StartAll ProgramsSlicer4.0.1Slicer
Or launch the Slicer executable from Slicer4 directory

## Slide 6: Load Atlas & Fibers
Add Data in File Menu
  Select all files in DTI atlas folder
  Change description to FiberBundle for fibers
  No mask
  Okay!

## Slide 7: DTI Atlas & Fibers
Link slices
Enable threshold in Volume module
Example tracts:
  CC Genu
  CC Splenium
  Uncinate right hemi
  Arcuate left hemi
Not anatomically verified!!

## Slide 8: Fiber based Analysis
Analyze corresponding fiber locations across datasets via atlas
  Mapping into atlas
  Inverse map to sample fibers
  Compute fiber profiles
    FA, MD, AD, RD…
  Analyze the profiles
Atlas Fiber

## Slide 9: DTI Property Fiber Profiles
Profile = Distribution of DTI values across fiber bundle
  Average & deviation
Parameterization of each fiber along fiber bundle
  Uniform stepsize
  Origin definition
    Manual
    Automatic (2 ways)
0
+L
-L

## Slide 10: DTI Atlas Fiber Analyzer
Separate tool called from Slicer
  Diffusion
  FiberAnalysis
  DTI Atlas Fiber Analyzer
Create new command line module
Apply!

## Slide 11: DTI Atlas Fiber Analyzer
Made for analyzing many datasets at once
.csv = comma separated value
Data can be prepared with Excel or other editors
Tabs for the 4 main steps
Load prior csv file
DataTable Area

## Slide 12: Step 1: Data Definition I
Create your datatable from scratch
1 row for 1 dataset
3 columns
  SubjectID
  Path to volume
  Path to Deformation
“Apply” to create the datatable

## Slide 13: Step 1: Data Definition II
Double click headers to edit
Set Subject Column to 1
Set dataset column to 2
Set deformation column to 3
Double click on “no data” to browse for datafile
Double click on “no deformation” to browse for deformation file

## Slide 14: Save the CSV Data
Save CSF File
Set Output folder for processing data
Next Step

## Slide 15: Step 2: Atlas Definition
Set Atlas to tutorial atlas
  Available fibers are automatically detected
Select fibers to be analyzed
  Add Genu or Add All
“Apply” to run, if data exists, asks about rerun
“Next”

## Slide 16: Step 3: Fiber Profiles
Manual vs Auto origin
  Autodetect if in atlas
    None here
Properties
  Select FA
“Apply” to run & wait, then “Next”

## Slide 17: Step 4: QC with Plots
Select Genu stat
And “Plot”
Plot-Window
Fiber Parametrization

## Slide 18: Step 4: QC with Plots II
Enable Atlas
  Profile should have similar shape

## Slide 19: Stats in Summary CSV
Fiber profiles are all gathered in single CSV
Use Excel for plotting
Use your favorite stats tool for analysis
  FADDTS: Zhu et al
You can merge results back with parametrized fiber
  Last Step: MergeStatWithFiber

## Slide 20: Example: Profiles in Excel

## Slide 21: Taste of Visualization
Load parameterized genu fiber
  Add Data => Model
Enable scalars and use FiberLocationIndex

## Slide 22: Example: Visualization of fiber tract statistics
Visualization in Slicer or ParaView
Add a model of brain surface for effect

## Slide 23: Conclusions
Fiber profile analysis with Slicer
  DTI Atlas Fiber Analyzer
  Registration to atlas needed
Future: An easy-to-use stats tool

## Slide 24: Acknowledgment
National Alliance for Medical Image Computing NIH U54EB005149
UNC: Jean-Baptiste Berger, Clement Vachet
Utah: Guido Gerig, Sylvain Gouttard