## Slide 1: Diffusion Tensor Processing and Visualization
Guido Gerig
University of Utah
NAMIC: National Alliance for Medical Image Computing

## Slide 2: Acknowledgments
Contributors:
C-F. Westin
A. Alexander
G. Kindlmann
L. O’Donnell
C. Goodlett
J. Fallon
R. Whitaker
R. McKinstry
National Alliance for Medical Image Computing (NIH U54EB005149)

## Slide 3: Diffusion Tensor Imaging (DT MRI) reveals White Matter Structure
Gray matter
White matter
Courtesy of Susumu Mori, JHU
DT MRI

## Slide 4: Diffusion in Biological Tissue
Motion of water through tissue
Sometimes faster in some directions than others
Anisotropy: diffusion rate depends on direction
isotropic
anisotropic
G. Kindlmann
Kleenex
newspaper
Notes: A basic characteristic of biological tissue is that water molecules move through and within it,
in a process called diffusion
Some materials have the interesting property that diffusion happens faster in some directions that others.
I’m demonstrating that here with some scans of inkblots I made on two kinds of materials, kleenex, and newspaper.
In kleenex- the ink spreads at same rate in all directions,
But newspaper has a preferred direction where the ink moveks faster.
The name for this phenemon is “anisottropy”.
The wider the variation in diffusion rate as a function of direction, the more “anisotropic” a material is,
This one-dimensional family of ellipses represents some of the different levels of anisotropy which can occur in 2D

## Slide 5: Diffusion in White Matter
Diffusion of water molecules
Reflects the underlying structure of the tissues
  Faster diffusion along fibers than perpendicular to them
  Water diffusion anisotropy used to track fibers, estimate white matter integrity
Tensor model [Basser]
  Determine the whole tensor to estimate diffusion anisotropy
From Beaulieu[02]

## Slide 6: The Physics of Diffusion
Density of substance changes (evolves) over time according to a differential equation (PDE)
Change in density
Derivatives (gradients) in space
Diffusion – matrix, tensor
(2x2 or 3x3)

## Slide 7: Solutions of the Diffusion Equation
Simple assumptions
  Small dot of a substance (point)
  D constant everywhere in space
Solution is a multivariate Gaussian
  Normal distribution
  “D” plays the role of the covariance matrix
This relationship is not a coincidence
  Probabilistic models of diffusion (random walk)

## Slide 8: Eigen Directions and Values (Principle Directions)
l1
l2
l3
v3
v2
v1
v1
v2
l2
l1

## Slide 9: Tensors From Diffusion-Weighted Images
Big assumption
  At the scale of DW-MRI measurements
  Diffusion of water in tissue is approximated by Gaussian
    Solution to heat equation with constant diffusion tensor
Stejskal-Tanner equation
  Relationship between the DW images and tensor D
kth DW Image
Base image
Gradient direction
Physical constants
Strength of gradient
Duration of gradient pulse
Read-out time

## Slide 10: DWI summary: Model
Single Tensor Model (Basser 1994)
A0
gi
Ai
D
Dxx
Dxy
Dxz
Dyy
Dyz
Dzz
Tensor
estimation

## Slide 11: Shape Measures on Tensors
Represent or visualization shape
Quanitfy meaningful aspect of shape
Shape vs size
Different sizes/orientations
Different shapes

## Slide 12: Measuring the “Size” of a Tensor
Length – (l1 + l2 + l3)/3
  (l12 + l22 + l32)1/2
Area – (l1 l2 + l1 l3 + l2 l3)
Volume – (l1 l2 l3)
Generally used.
Also called:
“Mean diffusivity” <MD>
“Trace”
Sometimes used.
Also called:
“Root sum of squares”
“Diffusion norm”
“Frobenius norm”

## Slide 13: ADC versus Mean Diffusivity
Apparent diffusion coefficient (ADC) measures diffusivity in a specific direction.
Mean diffusivity (<MD>) is the trace of the diffusion tensor.
Terms often not properly used, papers often cite ADC but actually mean <MD>
b0 g1 g2 g3 g4 g5 g6 FA MD
ADC in gradient directions
Trace

## Slide 14: Reducing Shape to One Number Fractional Anisotropy
FA increasing
Properties:
Normalized variance of eigenvalues
Difference from sphere
Invariant to size
FA does not uniquely characterize shape

## Slide 15: Tensor size (MD) and shape (FA)
Mean diffusivity (MD)
Fractional anisotropy (FA)
Isotropic
diffusion
Highly
directional diffusion
0
1
Low
High
White
matter
Cerebrospinal
fluid

## Slide 16: FA as an Indicator for White Matter
Visualization – ignore tissue that is not WM
Registration – Align WM bundles
Tractography – terminate tracts as they exit WM
Analysis
  Axon density/degeneration/integrity
  Myelin
Big question
  What physiological/anatomical property does FA measure?

## Slide 17: Visualizing Tensors: Direction and Shape
Color mapping
Glyphs

## Slide 18
Principal eigenvector, linear anisotropy determine color
e1
R=| e1.x |
G=| e1.y |
B=| e1.z |
Coloring by Principal Diffusion Direction
C. Pierpaoli, 1997
Axial
Sagittal
Coronal
Slide G. Kindlmann
Notes: Okay, some previous work on this specific problem of diffusion tensor visualizatoin.
There has been a lot of work in the medical community in how to look at SLICES of tensor data,
One popular way is based on simplifiying the whole tensor down to a single vector, specifically,
By looking only at the tensor’s principal eigenvector.
You use that direction as a lookup into some spherical colormap, like this one.
There’s a second step, which is to darken or desaturate the color where the anistoropy is low,
and then you can pretty clearly see the various structures inside the white matter.

## Slide 19: Issues With Coloring by Direction
Set transparency according to FA (highlight-tracts)
Coordinate system dependent
Primary colors dominate
  Perception: saturated colors tend to look more intense
  Which direction is “cyan”?
  Coloring is not unique

## Slide 20: Visualization with Glyphs
Density and placement based on FA or detected features
Place ellipsoids on regular grid

## Slide 21
Backdrop: FA
Color: RGB(e1)
G. Kindlmann
Notes: Combining these, we’re using ellipsoidal glyphs to indicate the tensors in this one small region around the splenium of the corpus callosum.

## Slide 23: Prolate vs. oblate: Why do we care?
Free diffusion (ventricles) shown as spheres.
Intersecting tracts can’t be properly modeled by a single tensor: Simplified to disks in rank-1 tensors.
Large tracts can be locally modeled by single tensors.
e3
e1
e2
1 2 3 - Isotropic
Prevalent in CSF and gray matter regions of the brain.
1 2>> 3 - Oblate
Arise in white matter regions.
1>> 2 3 - Prolate
Prevalent in white matter regions.
e2
e3
e1
e1
e2
e3

## Slide 24: Shape Other Than Size
1
2
3
l1 >= l2 >= l3
Barycentric
shape space
(CS,CL,CP)
Westin, 1997
G. Kindlmann

## Slide 25: Shape Characterization: Westin
Westin et al., MICCAI’99

## Slide 26: Dream: Connectivity?
Tractography: Coronal view (Dell’Acqua et al. NeuroImage ‘10
Source: Duke NeuroAnatomy Web Resources (Ch. Hulette)
Forebrain Fiber Bundles: General idea of where various fiber bundles are and regions they interconnnect or project to.

## Slide 27: Networking and Brain Connectivity
Major Fiber Tracts extracted from DT MRI
UNC Computer Science: Network wire cabinets

## Slide 28: White Matter Tracts
In tractography fibers are traced, with the aim to visualize white matter tracts.
The word “tractography” is not related to “tracking”, but to “tract”.
White matter tract, white matter fasciculus
Courtesy Carl-Fredrik Westin, MICCAI 2008 workshop

## Slide 29: Fiber Bundles via Tractography
Geng, Gilmore, Gerig et al., submitted

## Slide 30: From Tensors to Connectivity?
Study diffusivity in 3D tensor field
Propagate principal diffusion direction originating at user-selected seed point
Display paths as streamlines
Measurement of FA and MD along path

## Slide 31: DTI Tractography
Seed point(s)
Move marker in discrete steps and find next direction
Direction of principle eigen value

## Slide 32: Going Beyond Voxels: Tractography
Method for visualization/analysis
Integrate vector field associated with grid of principle directions
Requires
  Seed point(s)
  Stopping criteria
    FA too low
    Directions not aligned (curvature too high)
    Neighborhood coherence
    Leave region of interest/volume
Many methods have been published during the past decade (Basser, Mori, Westin, Vermuri, Kindlmann, Lenglet, etc.)

## Slide 33: White Matter Fiber Tract Atlases
Catani et al., Occipito-temporal connections in the human brain, Brain 2003

## Slide 34: The Problem with Tractography How Can It Work?
Integrals of uncertain quantities are prone to error
  Problem can be aggravated by nonlinearities
Related problems
  Open loop in controls (tracking)
  Dead reckoning in robotics
Wrong turn
Nonlinear: bad information about where to go

## Slide 35: Alternative methods for tractography
Tracking in vector-field of largest eigenvector
Tracking in tensor field
Probabilistic tractography
Optimal path analysis
Fiber tract by volumetric diffusion
….
Variety of methods developed by NAMIC developers
Georgia Tech: Opt. Path between source & target

## Slide 36: Diffusion MRI Tractography
Courtesy Carl-Fredrik Westin, MICCAI 2008 workshop

## Slide 37: Tractography Incorporating Uncertainty
Courtesy of Bruce Pike, MNI

## Slide 38: Stochastic Tractography
Lazar, Alexander, White Matter Tractography using Random Vector (RAVE) Perturbation, ISMRM 2002
D. Tuch, Diffusion MRI of complex tissue structure, Ph.D. dissertation, Harvard-MIT, 2002
Brun, Westin, Regularized Stochastic White Matter Tractography Using Diffusion Tensor MRI: Monte Carlo, Sequential Importance Sampling and Resampling. MICCAI 2002.
Zhang, Hancock, Goodlett and Gerig, Probabilistic White Matter Fiber Tracking using, Particle Filtering and von Mises-Fisher Sampling, Med Image Anal. 2009 Feb;13(1):5-18
Courtesy Carl-Fredrik Westin, MICCAI 2008 workshop

## Slide 39: Stochastic Tractography
Courtesy Carl-Fredrik Westin, MICCAI 2008 workshop

## Slide 40: Probability of Connection
Courtesy Carl-Fredrik Westin, MICCAI 2008 workshop

## Slide 41: Tractography
J. Fallon

## Slide 42: Probability of Connection
Courtesy Carl-Fredrik Westin, MICCAI 2008 workshop

## Slide 43: Modeling of fiber tracts
Origin (anatomical landmark)

## Slide 44: Example Uncinate Fasciculus
Corouge et al. Fiber tract-oriented statistics for quantitative diffusion tensor MRI analysis. Medical Image Analysis 2006.
FiberViewer software - http://www.ia.unc.edu/dev/

## Slide 45: Quantitative Tractography
- Tractography for ROI definition
- Tensor-math. for statistics along tracts
FA along tracts
Tract ROIs
Tensors statisics along spines
FA motor tract
MD motor tract

## Slide 46: Group testing of FA along motor tracts (Downs Syndrome vs. HC)
Center: Left and right motor tracts, color-coded with FA (0 to 1 in blue to red)
Left and right: FA as function of arc- length for HC (red) and DS (blue)
p < 0.03
DS .42 < HC .46
p < 0.0017
DS .47 < HC .52

## Slide 47: Summary: What do we measure?
DWI measures local diffusivity pattern.
Local diffusivity pattern is shaped by tissue type, axon structuring, myelination etc.
Curves and streamlines from tractography are NOT AXONS but possible paths in vector/tensor field.
“Fiber counting” scientifically questionable, # is method specific.
DWI DOESN’T MEASURE AXONS or GLOBAL CONNECTIVITY !

## Slide 48: Limitation of Tractograpy: Infer global structures from local estimates
Courtesy Carl-Fredrik Westin, MICCAI 2008 workshop
We measure diffusion structure of local elements (2x2x2mm3) and make inference/guess about road network → axonal bundles.
Voxel size: cubic mm
Axon diameter: micrometers

## Slide 49: Ermerging New Techniques: HARDI, DSI, Q-Ball
Wendell JS Krieg, 1963
DSI, 2008
VJ Wedeen, R Wang, T Benner
MGH-Martinos Center,Harvard Medical School

## Slide 50: Simplification and assumption
Diffusion ellipsoid
Courtesy of Susumu Mori, JHU
Orientational Diffusion Fct

## Slide 51: Limitations of the Diffusion Tensor Model
Courtesy B. Vemuri, MICCAI 2008 workshop

## Slide 52: DTI with 12 directions & 2 averages Crossing Fibers Dropout on FA
Courtesy R. McKinstry

## Slide 53: Motivation: Why higher order?
Courtesy Baba Vemuri, MICCAI 2008 workshop

## Slide 54: Orientation Distribution Function ODF
Courtesy Rachid Deriche, MICCAI 2008 workshop

## Slide 55: Two Tensor Model (C-F Westin, S Peled, G Kindlmann)
Courtesy Carl-Fredrik Westin, MICCAI 2008 workshop

## Slide 56: Centrum Semiovale corpus callosum (red) & corticospinal tract (blue)
DTI DSI
Wedeen / Wang /AGS / MGH - HST

## Slide 57
DTI
MGH / DT

## Slide 58
QBI
MGH / DT

## Slide 59
60 DW directions, Cardiac Gated, Scan time = 20 min, b = 3000 s/mm2
Spherical Deconvolution Tractography
Dell’Acqua et al. NeuroImage 2010

## Slide 60
Spherical Deconvolution Tractography
DTI Tractography
60 DW dir, Cardiac Gated, b=1500 s/mm2
Spherical Deconvolution Tractography
Close to standard DTI protocols
Dell’Acqua et al. NeuroImage 2010

## Slide 61: Q-Ball DTI
Delineation of Motor Tract
in Adult Brain Tumor
Patient
J.I. Berman, Diffusion MR Tractography as a Tool for Surgical Planning.
Mag. Res. Imag. Clinics of North America. 2009

## Slide 62: Brain Tumor Case
Courtesy Carl-Fredrik Westin, MICCAI 2008 workshop
Tractography based on higher-order tensor models and modeling of crossings and disperging bundles is vital for neurosurgical applications.

## Slide 63: Acknowledgments
Contributors:
C-F. Westin
A. Alexander
G. Kindlmann
L. O’Donnell
C. Goodlett
J. Fallon
R. Whitaker
R. McKinstry
National Alliance for Medical Image Computing (NIH U54EB005149)