## Slide 1: Slicer3 Tutorial Atlas Registration & Label Merging
Dominik Meier, Ron Kikinis
February 2010

## Slide 2: Overview
Introduction
Prerequisites
Modules Used
Loading Example Dataset 1 min
Viewing Input Data 3 min
Build Thalamus Mask Images 10 min
Build Thalamus Surface Models 3 min
Register Surfaces 3 min
Apply Transform 5 min
Mask & Clip 5 min
Merge Labels & Save 5 min
takes how long to do?
Note: if wish to skip parts of the tutorial, you will find the data generated by individual steps in the Example Data Folder. You may load these individually via the “File/Add Data…” menu.
The SlicerScene file that comes with the tutorial will only load the initial volume data.

## Slide 3: Introduction / Scenario
We have two anatomic atlases, obtained from two separate individuals by expert radiologist tracing. We refer to them as A0 (“old atlas”) and A1 (“new atlas”)
The “old atlas” A0 contains labels for 25 thalamic nuclei and substructures that are not present in the “new atlas” A1.
We want to transfer these labels from A0 -> A1, i.e. obtain a best possible estimate about the thalamic nuclei in A1 based on the information in A0
To this end we co-register the two atlases such that the thalamus of both align as good as possible. Then we merge the two label maps.
Because the two atlases hail from different individuals, no perfect alignment can be expected.
Because we’re interested only in the thalamus, we seek optimal alignment there and do not care much about the rest of the brain.
“Old Atlas” contains Thalamic Nuclei
animated GIFs: view in Presentation Mode
“New Atlas” does not

## Slide 4: Modules Used
To accomplish this task we will use the following modules:
  Editor (thresholding)
  Editor (change island)
  Python Surface ICP Registration
  Mask Image
  Cast Image
  Label merge
  Color
  Models

## Slide 5: Prerequisites
Slicer version 3.5 or later
Example Dataset: download and extract the dataset for this tutorial: Slicer_AtlasMerge.zip. It should contain:
  ManualRegTutorial.ppt Power Point File with this tutorial
  ManualRegTutorial.pdf PDF with this tutorial
  AtlasMergeTutorial_SlicerScene.mrml Slicer Scene File to load
  A0_gray.nrrd, A1_gray.nrrd grayscale images of both atlases
  A0_label.nrrd, A1_label.nrrd labelmap images of both atlases
Tutorials to complete first (helpful but not required):
  Slicer3Minute Tutorial
  Loading and Viewing Data
  http://www.slicer.org/slicerWiki/index.php/Slicer3.4:Training

## Slide 6: 1. Loading Example Dataset
To get the Example Dataset loaded into Slicer:
Menu: File: Load Scene…
  Select the Slicer Scene file that comes with the downloaded example dataset, called: AtlasMerge_SlicerScene.mrml
  This will load all the necessary images
Select Layout: From the icon bar, click on the Layout menu and select “Conventional Layout”.
Link Views: Click on the Ring Icon in any of the slice views to link all the views together. This will save you the work of making selections for each slice window separately.
Choose Foreground: A0_gray
Choose Background: A1_gray
Choose Labelmap: A1_labels

## Slide 7: Adjust Slice Views
To get an idea of the initial data and misalignment, perform the following to see both datasets in one image:
Adjust the labelmap opacity to see both the grayscale image and the labelmap.Set the slider to about 0.7
Set Visibility Slider to halfway between foreground and background. This allows you to see both atlases. You can see the initial misalignment.

## Slide 8: Build Thalamus Mask
For registration we need a model of the entire thalamus. Hence we must first merge the labels of all the nuclei
Turn off all display other than A0_labels, i.e. select “None” for fore- & background.
The current colormap shows all nuclei labels as green. To see the individual structures, we select a new colormap: Go to the Volumes Module.
As “Active Volume” select “A0_labels”
Under “Lookup Table”, select “Labels From File” and “SPL-BrainAtlas-ColorFile.txt”

## Slide 9: Build Thalamus Mask (2)
Via the right mouse button, zoom in. You should see the individual nuclei. If you hover the mouse over each, the label and number are displayed under “Lb:
All thalamic structures have labels from 500-525. We use this to merge them into a single mask volume.

## Slide 10: Build Thalamus Mask (3)
Go to the “Editor” module
Under “Create Labelmap From”, select “A0_labels”
Under “Select Labelmap to Edit”, select the newly created “A0_lables-label” and then select “Rename”. Rename the new volume to “A0_thalamus”
From the icon panel, select the “Threshold Icon”

## Slide 11: Build Thalamus Mask (4)
In the numeric fields, type the range: 500 and 525. You will see the selected structure “blink” in blue
Click on “Apply” to create the new volume

## Slide 12: Build Mask for New Atlas
Now we repeat the process to build the mask volume for the new atlas A1. A1 only has 2 labels for the left and right thalamus, respectively: 49 and 10. Because they are non-sequential we first change one.
In the Editor, for “Label Map to Edit”, select “A1_label”
Select the “Change Island Icon”
Change the label field to 49
In the axial view, left click in the yellow area representing the left thalamus. Upon the click, the area should become the same turquoise color as the right thalamus.

## Slide 13: Build Mask for New Atlas (2)
Now we repeat the thresholding to extract only label 49.
  For “Create Label Map From”, select “A1_label”. For “Select Label Map to Edit”, select new “A1_label-label”, and choose “Rename”. Rename to “A1_thalamus”
  Set the label field back to 1.
  Select the “thresholding” icon, and for the range enter 49 in both fields.
  Hit Apply
We now have label volumes for the thalamus in both atlases.
Next we build models for both.

## Slide 14: Build Thalamus Models
Go to the “Model Maker” Module (under Surface Models).
For “Input Volume”, select “A0_thalamus”
For “Models”, select “Create New Model Hierarchy”, then select “Rename” and enter “A0_ThalamusModel”
In the “Labels” field, enter 1.
Set the “Smooth” iterations field to 50
Leave the “Decimate” field at the default of 0.25
Turn off “Split Normals” checkbox
Click “Apply”
After a few seconds of processing, you should see a model appear in the 3D view.

## Slide 15: Build Thalamus Models (2)
Before we build the second model, we apply some morphological cleanup to the second labelmap: Go to “Filtering / Denoising / MedianFilter” module. Select “A1_thalamus” as both input and output, leave defaults and click apply. The jagged edges at the surface will disappear.
We now Repeat the steps 1-9 on the previous slide for the second atlas, i.e. create “A1_ThalamusModel” from the “A1_thalamus” volume.
You should now have 2 models for each atlas, as seen on the right.

## Slide 16: Register Thalamus Model Surfaces
Go to the “Python Surface ICP Registration” module
Select “Affine” and “RMS” and “Start by matching centroids”
For “maximum number of iterations” and “landmarks”, set 200 each.
Input Surface: A0_ThalamusModel Target Surface: A1_ThalamusModel
Output transform: “Create New Linear Transform”, then select “Rename” and rename to “Xform_A0affine_ICP”
Click “Apply”.

## Slide 17: Register Thalamus Model Surfaces (2)
Go to the “Data” module
Select the node “A0_ThalamusModel” and drag it on top of the “Xform_A0affine_ICP” node
Click in the 3D view to force a redraw. You should now see the two models on top of each other.
Go to the “Models” volume.
Select “A0_ThalamusMode” from the menu, click on the “Set Color” button and change color to yellow.
Set the opacity slider to 0.9
Select “A1_ThalamusModel” and set the opacity to 0.7

## Slide 18: Apply Registration to Labelmap
Go to the “Resample Scalar/Vector/DWI Volume” module
Input Volume : “A0_labels” Reference Volume : “A1_labels” Output Volume : “Create New Volume”, rename to “A0_labels_aff”
Transform Node: “Xform_A0Affine_ICP”
Interpolation Type: “nn”
Click “Apply”.
Repeat for the “A0_Thalamus” volume, i.e. create a new “A0_Thalamus_aff”
Go to the “Volumes” module, select the newly created “A0_labels_aff” and “A0_thalamus_aff”, then check the “Labelmap” box.

## Slide 19: Mask New Labelmap
From the new labelmap we want to keep only the thalamic structures:
Go to “Mask Image” module
Input Volume: “A0_labels_aff” Mask Volume: “A0_thalamus_aff” Masked Volume: “A0_labels aff” (Note we overwrite the volume with the masked one, if you get an error at this step you need to repeat the previous resampling step)
Click “Apply”.

## Slide 20: Mask New Labelmap (2)
Finally we mask again with the thalamus of the new (target) atlas. This is to prevent replacing labels other than the thalamus in places where the registered volume extends beyond the target. In other words we clip off anything “sticking out” beyond the boundaries of the A1 thalamus:
Go to the “Mask Image” module
Input Volume: “A0_labels_aff” Mask Volume: “A1_thalamus_aff” Masked Volume: “Create New Volume”, rename to “A0_labels aff_clip”
Click “Apply”.

## Slide 21: Type Cast Atlas Labelmap
Go to the “Cast Image” module
Input Volume: “A1_label” Output Volume: “A1_label” Output Type: “short”
Click Apply
Some labelmaps can have different datatypes, which can cause problems when merging. To ensure both volumes to be merged have the same datatype we check the info in the “Volumes” module. To change we use the “Cast Volume” module”:

## Slide 22: Merge Labelmaps
Last step is to transfer the Thalamic Nuclei labels into the A1 labelmap.
Go to the “Image Label Combine” module
Input Label Map A: “A0_label_aff_clip” Input Label Map B: “A1_labels” Output Label Map: “Create New Volume”, rename to “A1_labels_merged”
Check box: First label overwrites second.
Click Apply
Go To “Volumes” module, select the new “A1_labels_merged” and check the “Labelmap” box.

## Slide 23: Save
Select “Save” from the File Menu.
Check all boxes except the original input images “A0_gray”, “A0_labels” etc.
Create a new output directory, and select it via the “Change Destination For All Selected” button.
click “Save Selected”.

## Slide 24: View Result
Go to the “Volumes” module, select “A1_label_merged”. Under “Display”, select a new colormap: “Labels from File / SPL-BrainAtlas-ColorFile.txt”
In the slice view, select “A1_gray” for for background, “A1_labels_merged” for labelmap.
Set the labelmap opacity to ~0.7

## Slide 25: What Next
Try the Manual Registration Tutorial or one of the tutorials from the Registration Case Library.
  http://www.slicer.org/slicerWiki/index.php/Slicer3.4:Training
  http://na-mic.org/Wiki/index.php/Projects:RegistrationDocumentation:UseCaseInventory
  http://www.slicer.org/slicerWiki/index.php/Slicer3:Registration#Registration_in_3D_Slicer|Main
Feedback: anything amiss? If you have suggestions on how we can improve this and other documentation, please let us know: visit:
  http://na-mic.org/Wiki/index.php/Projects:RegistrationDocumentation

## Slide 26: Acknowledgements
National Alliance for Medical Image Computing
NIH U54EB005149
Neuroimage Analysis Center
NIH P41RR013218 -12S1 (ARRA Suppl)