## Slide 1: Fractured Bone Position and Shape Estimation Based on Recursive 2-D/3-D Registration of Deformable Models
Y. Nakajimaa , T. Saitoa, S. Onogib , N. Sugitaa , H. Hashizumec, T. Inoued, K. Kuramotod , Y. Nakashimad , M. Mitsuishia
a School of Engineering, University of Tokyo, Tokyo, Japan
b Intelligent Modeling Laboratory, University of Tokyo, Tokyo, Japan
c Kasaoka Daiichi Hospital, Okayama, Japan
d Nakashima Medical Co., Ltd., Okayama, Japan
Toki Saito
Nakajima Laboratory
Department of Mechanical Engineering,
the University of Tokyo
Notes: <number>

## Slide 2: Background
A bone position is estimated by geometrically fitting 3D-CT image to X-ray images during a surgery.
  It is called as 2D/3D registration.
It is one of the promising methods for estimating a bone position.
X-ray image
2D/3D registration
3D-CT image
Position estimation
fitting
Notes: <number>

## Slide 3: Background
Some researchers proposed the 2D/3D registration method of using statistical deformable model instead of 3D-CT model.
Statistical models describe average shape and deformation, and can deform into all kinds of shape.
By using this model at 2D/3D registration, bone position and shape can be estimated at the same time, and this method has been confirmed in past.
Large
Small
Statistical deformable model
Jianhua Yao, Russell H. Taylor, “Assessing Accuracy Factor in Deformable 2D/3D Medical Image Registration Using a Statistical Pelvis Model”, IEEE International Conference on Computer Vision (ICCV), pp 1329-1334, 2003.
X-ray image
Statistical deformable model
fitting
Deformation
Notes: <number>

## Slide 4: Problem
It is difficult for deformable models to apply any cases of fractures, since
  shapes of broken parts and condition of repositioning are various, and
  a deformable model is generally created from healthy bones.
3D-CT models of healthy bones
Deformation
Large
Small
Deformable model
:statistical model : mean
:eigen vector :magnitude
:number of eigen vector
Fractured bones
Reduced bone
Notes: <number>

## Slide 5: Purpose
We propose a deformable-model-based 2D/3D registration method which supports fractured bone.
The method provides the reduced bone shape and fragment’s positions.
Notes: <number>

## Slide 6: Method
The initial shape of a statistical model is set to the average shape of the model.
X-ray source
X-ray projection line
X-ray image
A statistical model
Bone fragments
(unknown)
Image contours
Notes: <number>

## Slide 7: Method
T1
T2
Position estimation
2. 2D/3D registration is applied to each contour, and fractured bone positions, T1 and T2, are estimated.
Each position is optimized by minimizing sum of distance d between X-ray projection lines of each contour and bone model.
:temporal position matrix of a fragment
:number of projection line at each contour
:each distance between 3-D model and a projection line
X-ray source
X-ray projection line
X-ray image
Image contours
Notes: <number>

## Slide 8: Method
3. The bone model, V, is deformed as matching all contours and the model surface geometrically by using the temporal translational matrices of the fragments.
The inverse matrices of T1 and T2 enable us to reconstruct a reduced bone contour.
:temporal position matrix of a fragment
:number of projection line at each contour
:each distance between 3-D model and a projection line
T1-1
T2-1
Shape estimation
:bone shape
V
reconstructed contour
Notes: <number>

## Slide 9: Method
T1
T2
Position estimation
T1-1
T2-1
Shape estimation
Iteration until convergence
Iteration until convergence
4. Step 2 and step 3 are repeated until convergence.
At each process, estimated positions and estimated bone shape are recursively used. This method is based on the mathematical manner of projection onto convex sets (POCS).
V
Notes: <number>

## Slide 10: Experiment
We have validated the proposed method in terms of
  the ability of the deformable model for describing various bone shapes,
  the accuracy of position estimation, and
  the convergence ratio of the computation.
Notes: <number>

## Slide 11: Experiment
Leave-one-out cross validation
  Scaphoid surfaces were made from the CT-images of 37 healthy volunteers.
  A surface was selected. A statistical model was made from the other 36 surfaces, and then was deformed as fitting its shape to the selected surface.
  The error of the deformation was validated by computing the volume difference between them.
  Evaluating for each of the 37 patterns of selection, the statistical value of the errors can be obtained.
‥‥‥
A statistical model
(made from the other 36 surfaces)
Shape estimation
  Leave-one-out cross validation method
A selected surface
Notes: <number>

## Slide 12: Experiment
Experiment condition
The condition of X-ray photography
  Imaging directions： Front and left side
  Angle：90 degrees
The condition of X-ray image
  Number of bone fragments：2
  Pixel size：512×512
  Number of contour points：150～200
  Target: Wrist bone (scaphoid)
Imaging direction
Z
Y
X
X
Y
Z
X-ray image
Frontal
Lateral
Notes: <number>

## Slide 13: Result
Shape error
Position error
 | Volume error[%] | probability of divergence[%]
Proposed method | 10.9 | 0.3
Normal method | 31.7 | 0.0
 | Degree error[deg] | Position error[mm] | probability of divergence[%]
Proposed (fracture 1) | 7.5 | 1.0 | 6.6
Proposed (fracture 2) | 16.2 | 0.9 | 26.0
Normal | 26.8 | 4.7 | 0.0
Notes: <number>

## Slide 14: Discussion
Shape estimation error is decreased from 31.7% to 10.9%.
Probability of divergence in proposed method is higher than it in normal method.
  Because each fragment position is estimated as matching its contour and bone surface, and the magnitude of the constraint in computation was decreased. This problem would be fixed by introducing anatomical constraint around scaphoid.
Normal method
Proposed method
T1
T2
X-ray source
X-ray projection line
T
X-ray source
X-ray projection line
Notes: <number>

## Slide 15: Conclusion
We propose a deformable-model-based 2-D/3-D registration method which supports fractured bone.
This method provides
reduced shape from X-ray images of a fractured bone,
positions of respective bone fragments, and
relative position of bone fragments.
Notes: <number>

## Slide 16: Thank you very much for your attention
Notes: <number>

## Slide 17
Shape error
Red area＋blue area
Red area
Estimated shape
Correct shape
Notes: <number>