## Slide 1: NAMIC Work at BU: Interactive Segmentation/Multi-Atlas Driven Coupled Segmentation/Registration
Peter Karasev, Ivan Kolesov, Xerogeanes, Allen Tannenbaum
Yi Gao and Allen Tannenbaum

## Slide 2: Expert Knowledge for Segmentation
A motivating problem: measuring volume of Epiphysis, Cartilage-Cap, and Physis (growth-plate) during adolescence.
Left: automatic segmentation of Epiphysis.
Right: augmentation by user-in-the-loop curve evolution.
Notes: Automatic segmentation methods will have some error.
We want to be able to see the result and make minor corrections.
Don't want to smoothen everything and lose detail.
Don't want to think about clever "erode, dilate, merge, threshold, erode" sequences of operations.
One user-set parameter: "paint-brush size".

## Slide 3: Video Demos

## Slide 4: Why Interactive Segmentation?
  Ever more complex segmentation models will be slower and still not work in many cases.
  Atlas-Based methods may not be applicable (trauma, unique growth stage, atlas is "To-Do")
  Doctors & Med Students can use it easily, sole parameter is "editor brush size".
Above: Timeline of Interactive Segmentation System
Notes: Atlas-based methods are good, but we may not have an atlas. With the knee, we're trying to construct an atlas in the first place.
User draws some initial seed blob, presses "s" a few times to evolve contour. Draw some fixes, evolve some more.
***Anatomic boundary is not the local minima of anything! Only of some magic "doctor functional" ***
We can actually approximate this magic doctor functional by writing the contour energy minimized to include user input!

## Slide 5: Formulation: Augmented Cost-Function
  Nominal cost function
    minimizing this is "automatic algorithm"
  User-Input: changes to segmentation function at discrete intervals
  Augmented Curve Evolution
    nominal plus user-driven term
  Signal Definitions
    User Input Error
    Observer Error
Notes: This slide introduces some notation.
Nominal cost is "Local-Global" for the shown examples. See Shawn's paper for definition of the "G" gradient flow.
U is the accumulated user input. The more times user re-draws in one spot, the greater the U.
If there is zero user input, phi^* will simply follow the "automatic" evolution of phi.
Two error signals: between user input and observer, and between displayed segmentation and observer.

## Slide 6: System Diagram with Feedback Loops
Notes: When we press "s" key, some iterations of inner loop occur, generating updated segmentation for display.
Seeing this result, user can inject more input if desired.
Because we're integrating the user input, the automatic evolution won't "overwrite" their modifications; rather, the user is changing the steady-state set-point of the evolution.
Steady-state local-min is satisfied when the user stops injecting energy; ideal segmentation is achieved.

## Slide 7: Sample Workflow
2020 Label maps interactively drawn by medical student in "down-time" while on rotations!
Notes: Meta-physis (long bone), Physis (growth-plate), and Epi-physis are shown segmented.

## Slide 8: Sample of Left Atrium Segmentation

## Slide 9: Brain Segmentation

## Slide 10: Blood pool
Atlas based segmentation
  Target image I
  Training images J1, …, JN; their label images L1, …, LN
Affine register J1 to I
Focus on heart region
BSpline registration
Deform L1
Transform L1
Affine register JN to I
Focus on heart region
BSpline registration
Deform LN
Transform LN
K1, c1
KN, cN
Afib Segmentation

## Slide 11: One result case
3D |  | 3D
Axl | Sagi | Coro

## Slide 12: Result
The module has been tested by Utah people and the walls are segmented, for example:
Manual wall
Auto wall
http://wiki.namic.org/Wiki/index.php/DBP3:Utah:AutoWallSeg

## Slide 13: Other Projects
Bhattacharyya Registration for TBI
Sparse Active Contours
Stochastic Based/Particle Filtering Registration for Adaptive Radiotherapy