## Slide 1
Segmentation for 3D printing
Csaba Pinter
Queen’s University, Canada
csaba.pinter@queensu.ca
NA-MIC Tutorial Contest: Winter 2017
© 2017, All Rights Reserved

## Slide 2: Learning Objective
This tutorial demonstrates segmentation in Slicer’s new Segment Editor module for the purpose of 3D printing
© 2017, All Rights Reserved

## Slide 3
This tutorial requires the installation of a recent Slicer 4.7 nightly release, which is available at the
Slicer download page:
http://download.slicer.org/ (see row of Nightly Build)
Tutorial dataset: Phantom base STL model
http://www.na-mic.org/Wiki/images/1/1e/BasePiece.stl
Wiki pages:
https://www.slicer.org/wiki/Documentation/Nightly/Modules/Segmentations
https://www.slicer.org/wiki/Documentation/Nightly/Modules/SegmentEditor
Material
© 2017, All Rights Reserved

## Slide 4
Developed and maintained on Windows 64bit, Mac OSX, and Linux 64bit & 32bit
Slicer requires
  Minimum 2GB RAM
  64 bit strongly suggested
Platforms
© 2017, All Rights Reserved

## Slide 5
Successor of the ‘Editor’ module
In addition to Editor it provides
  real-time 3D surface update
  editing on oblique slices
  overlapping segments, and much more
It is considered stable
  But development is still underway
Segment Editor module
© 2017, All Rights Reserved

## Slide 6
Load CT image
Segment vertebrae to be 3D printed
Add phantom base to segmentation
Merge and finalize phantom
Save phantom segment to STL file for 3D printing
Overview
© 2017, All Rights Reserved

## Slide 7: Part 1: Load CT image
Overview:
Load sample CTChest dataset
Set image contrast for better visibility
© 2017, All Rights Reserved

## Slide 8: 1/1: Load CTChest dataset
© 2017, All Rights Reserved

## Slide 9: 1/2: Sample CT loaded
© 2017, All Rights Reserved

## Slide 10: 1/3: Change contrast
Select CTChest as active volume
© 2017, All Rights Reserved

## Slide 11: Part 2: Segment vertebrae
Overview:
Add new segment
Threshold bone
Remove speckles with Islands
Cut out vertebrae with Scissors
© 2017, All Rights Reserved

## Slide 12: 2/1: Switch to Segment Editor module
© 2017, All Rights Reserved

## Slide 13: 2/2: Add new segment
- Segmentation automatically created
- CT volume automatically selected as master
(Master is the segmented volume that defines the resolution of the segments)
© 2017, All Rights Reserved

## Slide 14: 2/3: Threshold to get bone
Set 100
© 2017, All Rights Reserved

## Slide 15: 2/4: Remove speckle with the Islands effect
Select Islands effect
© 2017, All Rights Reserved

## Slide 16: 2/5: Remove speckle with the Islands effect
© 2017, All Rights Reserved
Click on spine

## Slide 17: 2/6: Cut out vertebrae with the Scissors effect
1. Select Scissors effect
2. Choose ‘Erase outside’ as operation
3. Choose ‘Free-form’ shape
© 2017, All Rights Reserved

## Slide 18: 2/7: Cut out vertebrae with the Scissors effect
Trace around the desired vertebrae with the scissor on the coronal view (green slice)
© 2017, All Rights Reserved

## Slide 19: 2/8: Show segment as surface in 3D view
© 2017, All Rights Reserved

## Slide 20: 2/9: Remove remaining parts with Scissors
Select the vertebrae in the 3D view to erase the remaining parts (ribs on the anterior side in this case)
© 2017, All Rights Reserved

## Slide 21: 2/10: Vertebrae are segmented
© 2017, All Rights Reserved

## Slide 22: Part 3: Add phantom base
Overview:
Load phantom base STL file
Transform model to desired position and orientation
Import model to segmentation node
Cut hole through middle of the spine
© 2017, All Rights Reserved

## Slide 23: 3/1: Load phantom base as model node
Download phantom base STL file from http://www.na-mic.org/Wiki/images/1/1e/BasePiece.stl
Drag&drop ‘BasePiece.stl’ onto the Slicer
© 2017, All Rights Reserved

## Slide 24: 3/2: Load phantom base as model node
© 2017, All Rights Reserved

## Slide 25: 3/2: Load phantom base as model node
© 2017, All Rights Reserved
Phantom base is loaded

## Slide 26: 3/1: Make base semi-transparent in Models
© 2017, All Rights Reserved
When both the segmentation and the model are opaque, it is hard to see when they are in a good relative position
1. Switch to Models module
2. Decrease opacity to 0.8

## Slide 27: 3/2: Create transform
© 2017, All Rights Reserved
1. Switch to Transforms module
2. Create linear transform 3. Name it ‘SpineToBaseTransform’

## Slide 28: 3/3: Apply transform to base
© 2017, All Rights Reserved
1. Select base piece
2. Move it under the tansform

## Slide 29: 3/5: Move base into place
© 2017, All Rights Reserved
1. Decrease minimum value to -400
2. Move sliders until the base is in the correct position (values in picture are the final ones)

## Slide 30: 3/6: Base is in the correct position
© 2017, All Rights Reserved
But we need to remove some slack

## Slide 31: 3/7: Use Scissors effect to remove slack
© 2017, All Rights Reserved
1. Back to Segment Editor
2. Erase slack

## Slide 32: Part 4: Merge and finalize phantom
Overview:
Create segmentation from base piece
Copy base piece segment into vertebrae segmentation
Merge two segments
Cut hole through phantom
© 2017, All Rights Reserved

## Slide 33: 4/1: Import base into segmentation
© 2017, All Rights Reserved

## Slide 34: 4/2: Import base into segmentation
© 2017, All Rights Reserved
Base piece is a surface, and the vertebrae were created as labelmaps. Convert to surface to allow import

## Slide 35: 4/3: Convert back to labelmap to allow editing
1. Make binary labelmap master again to allow editing in Segment Editor
2. Click yes in popup
© 2017, All Rights Reserved

## Slide 36: 4/4: Merge the two in Segment Editor
© 2017, All Rights Reserved
1
2
3
4
5
Back to Segment Editor

## Slide 37: 4/5: Remove base piece segment
© 2017, All Rights Reserved

## Slide 38: 4/6: Cut hole through phantom using Scissors
© 2017, All Rights Reserved

## Slide 39: 4/7: Phantom is ready

## Slide 40: Part 5: Save phantom to STL
Overview:
Export phantom segment to model node
Save model to STL file
© 2017, All Rights Reserved

## Slide 41: 5/1: Export phantom segment into model
Switch to Segmentations module

## Slide 42: 5/2: Save model into STL

## Slide 43
Segmentation and conversion to surface is now easier with the new Segment Editor and Segmentations modules.
Conclusion
© 2017, All Rights Reserved

## Slide 44
National Alliance for Medical Image Computing
NIH U54EB005149
Cancer Care Ontario
Acknowledgments
© 2017, All Rights Reserved
Ontario Consortium for Adaptive Interventions in Radiation Oncology