## Slide 1: DICOM to NRRD Conversion Tutorial
Jean-Baptiste Berger
University of North Carolina
Neuro Image Research and Analysis Lab

## Slide 2: DICOM to NRRD Tutorial
This tutorial guides you through the process of converting DICOM files into a NRRD volume file, loading a volume file, choosing a set of colors and saving the processed NRRD file.

## Slide 3: Dataset
For this tutorial you will need some DICOM data files that can be found on this link : http://hdl.handle.net/1926/1759

## Slide 4: Start Slicer4
Linux/Mac users :
Launch the Slicer
executable located in
the Slicer4 directory
Windows users :
Select StartAll ProgramsSlicer4.0.1Slicer
Or launch the Slicer executable from Slicer4 directory

## Slide 5: Welcome Module
The Slicer Welcome module is the
module displayed by default.
This module gives an overview of the
GUI of Slicer4, and data loading & saving
functionality.

## Slide 6: DICOMtoNRRD Module
Left click on the menu Modules and
select All Modules to display the list
of modules available for image
analysis and 3D visualization.
Select the module Dicom to Nrrd converter

## Slide 7: DICOMtoNRRD Module
Select the Input DICOM directory
Select the Output directory
Choose an Output name for your Nrrd file

## Slide 8: DICOMtoNRRD Module
Left click on Output Option to get it extended
Left click on the 3rd check box (If you leave the mouse near it, it will display the ToolTip)
Left click on Apply button

## Slide 9: Adding Nrrd Volume
Left click on file menu
Left click on Add Volume

## Slide 10: Adding Nrrd Volume
Select your previously created Nrrd volume

## Slide 11: Volumes
Left click on the volume icon

## Slide 12: Volumes
Select the volume you just opened in the “Active Volume” Section

## Slide 13: Volumes

## Slide 14: Saving your data
Left click on File
Left click on Save

## Slide 15: Saving your data
Select the Nrrd file
Select the Directory where you want to save it
Left click on Ok

## Slide 16: Conclusion
This tutorial guided you through the conversion from DICOM to NRRD file using Slicer 4 Software