## Slide 1: Image Processing Strategies
Image Biomarkers for Drug Discovery
Steve Pieper, PhD
Isomics, Inc.
http://www.isomics.com

## Slide 2: Goals
Overview of Medical Image Computing
  Issues
  Solution Approaches
Example Projects from Current Research Activities
  Emphasis on Custom Analysis Pipelines
  Open Science / Open Source Software
  Pointers to Additional Information

## Slide 3: Outline
Background
  Getting the Images
  Organizing the Images
  Working with the Images
Software
Examples
  Tumor Change Tracking
  Huntington’s Disease Tracking

## Slide 4: Clinical Image Data
Retrospective Analysis Opportunities
  Natural Disease Occurrence and Responses to Current Treatments
  Existing Data, Low Cost to Acquire & Analyze
Full Clinical Context Difficult to Acquire
  Multiple Databases in Different Departments
  Inconsistent Data Formatting

## Slide 5: Medical Image Informatics Bench to Bedside (mi2b2)
Builds on i2b2 (http://www.i2b2.org)
  Institution-Wide Medical Records Databases: Demographics, Visits, Observations, Labs, Medications, Diagnoses, Procedures…
  Query Software: Identify Patient Cohort
  IRB Compliance Support
Adds PACS Access
  Governed and Audited Access to Radiology Images
  Exported to Research Analysis Compute Resources
  4,000 Subject Baby Brain Study Underway
    Normative Atlas of White Matter Development in Early Years of Life
    First Example of Important Class of Research
Being Deployed at Harvard Hospitals with Catalyst
http://www.na-mic.org/Wiki/index.php/CTSC:ARRA_supplement

## Slide 6: Multi-Center Image Collection
Considerations
  Scanner Calibration of Sequences across Vendors and Models
  Standardized Acquisition Protocols, Terminology, and Data Formats
  Ongoing Calibration After Upgrades and Maintenance
  Standardized Pipelines for Data Cleanup and Analysis
  Statistical Methods for Identifying Site-Specific vs Subject Variability
Best Practices Cookbooks in MR
  Biomedical Informatics Research Network (BIRN)
  Guidelines for Structural, fMRI & dMRI
  THPs (Traveling Human Phantoms) Very Valuable
http://www-calit2.nbirn.net/research/morphometry
http://www-calit2.nbirn.net/research/function

## Slide 7: Organizing Images and Related Data
DICOM / PACS
  “Native” Format for Medical Images
  Often Does Not Support
    Emerging Imaging Types
    Derived and Non-Imaging Data
Open Image Informatics Tools
  XNAT – http://www.xnat.org
    Neuroimaging, fMRI…
  MIPortal - http://cmir.mgh.harvard.edu/bic/miportal
    Small Animal Imaging…
  MIDAS - http://midas.kitware.com/
    Digital Library…

## Slide 8: Visualization: Seeing the Images
Displays to Enhance Interpretation
Interactivity for Rapid Assessment of Large Collections of Images
Specialized Modes to Emphasize Features of Interest
  2D/3D Localized Changes
  Statistical Maps of Group Differences
  Display Conventions (Image Orientations, Color Coding, Interactive View Controls…)

## Slide 9: Registration: Change Detection
Identify Corresponding Anatomical Regions
  Linear and Non-Linear Mappings
Control for Normal Changes
  Pose in Scanner
  Metabolic Differences (Digestive/Respiratory/Cardiac Cycles, Weight Gain/Loss…)
  Scan Artifacts
Detect & Quantify Important Differences
  Pathology Growth/Shrinkage
  Functional Differences
  Overall Atrophy, Edema, Other Responses…
NA-MIC Use Case Library
  Dominik Meier, BWH
http://na-mic.org/Wiki/index.php/Projects:RegistrationDocumentation:UseCaseInventory

## Slide 10: Segmentation: Anatomical Labeling
Image Driven Tissue Differentiation
  Self-Referenced
  Atlas-Based
Basis for Region-Specific Change Quantification
  With Respect to Subject Baseline
  With Respect to Population
Software
  EMSegmenter, Kilian Pohl, University of Pennsylvania
  FreeSurfer, Bruce Fischl et al, Massachusetts General Hospital
http://surfer.nmr.mgh.harvard.edu/
http://slicer.spl.harvard.edu/slicerWiki/index.php/Modules:EMSegmenter-3.6

## Slide 11: User Intervention and QA
Fully Manual
  Protocols for Measurement
User-Steered
  Select Seed Point or Volume of Interest
Automated
  Highly Dependent on Acquisition Quality
QA
  Always Required to Detect and Fix the Failures of the Automated Methods
  Always Required to Detect and Fix the Failures of the Human Operators

## Slide 12: Image Processing Software
FDA Regulated Commercial Products
  Optimized for Existing Clinical Procedures
Research Software
  “Latest and Greatest”
  Often Inconsistently Validated and Supported
Open Source Software
  Many Varieties: Check License for Restrictions on Commercial Use (Not Truly “Open”)
  Arguably Greatest Flexibility and Community Support

## Slide 13: National Alliance for Medical Image Computing: http://www.na-mic.org
Over A Dozen Collaborating Institutions Delivering Open Platform
NIH Funded National Center for Biomedical Computing
Builds on Existing Open Software Technologies
  http://itk.org http://vtk.org http://python.org http://slicer.org http://cmake.org http://qtsoftware.org
Provides Integration, Training, Support
Develops Custom Algorithms for Driving Biological Projects

## Slide 14: 3D Slicer: http://slicer.org
Multi-OS End-User Application (Windows, Linux, Mac)
Medical Image Visualization and Analysis
  Multi-Modal: CT, MR, fMRI, dMRI…
  Integrated View: Images, Surfaces, Annotations, Devices…
Extensible Architecture
  Dozens of Custom Modules
  Application Specific Functionality
Fully Open and Non-Restrictive License
  All Source Code Available
  Can Be Used in Commercial or Proprietary Projects

## Slide 15: Change Tracker
3D Slicer Interactive Module
Workflow for Analysis of Small Volumetric Changes
  Between Two Time Points
  Same Acquisition Parameters
Investigators:
  Kilian M Pohl, PhD – University of Pennsylvania
  Ender Konukoglu, PhD – INRIA Sopia Antipolis
  Andriy Fedorov, PhD – Brigham and Women’s Hospital
http://www.slicer.org/slicerWiki/index.php/Modules:ChangeTracker-Documentation-3.6

## Slide 16: Evaluating Tumor Size and Shape
Established Techniques
  Uni-dimenional or Bi-dimensional Measurements
  RECIST (Response Evaluation Criteria in Solid Tumors)
Issues
  May Fail to Detect or Quantify Small Changes
  Difficult to Assess Volumetric Changes
Higher Sensitivity and Specificity Desired to Improve Statistical Power
  Reduce Number of Subjects
  Shorten Time Required for Significant Results
http://www.eortc.be/recist/documents/RECISTGuidelines.pdf

## Slide 17: Example: Meningioma
Acquisition:
  Axial 3D SPGR T1 Post-Gadolinium Scans (Voxel dimension: 0.94mm x 0.94mm x 1.20mm, FOV: 240mm, Matrix: 256 x 256)
  Homogeneous Contrast Enhancement in Both Time Points
Baseline Radiologist’s Clinical Impression
  Large Falcine Lesion is Identified
  Measures 3.1 cm Anteroposteriorly, 3.05 cm from Side-to-Side, 3.5 cm in Height
  Enhances Moderately on Post-Gadolinium Imaging
Follow-up Radiologist’s Clinical Impression
  Left Frontal Lobe Mass Appears Unchanged on all Series
  Measures 3.3 x 3.2 cm in Maximum Dimension
  Enhances Moderately on Post-Gadolinium Imaging
SCAN1
Baseline: June 2006
SCAN2
Follow-up: June 2007

## Slide 18: Steered Segmentation
Identify Volume of Interest
Select Enhancement Threshold

## Slide 19: Time Point Correlation

## Slide 20: Integrated Visualization
3D Rendering of Volume Change: magenta = growth green = shrinkage
Aligned Slice Views
Linked Crosshair for Image Exploration

## Slide 21: Pattern Analysis and Quantification

## Slide 22: PredictHD
Genetic and Imaging Study
  Detect Early Signs of Huntington’s Disease
NA-MIC Collaboration with
  Hans Johnson and Colleagues at University of Iowa
http://www.predict-hd.net/

## Slide 23: Motivations
HD is a Neurodegenerative Disease
  Affects Muscle Coordination, Behavior, and Cognitive Function
  Causes Severe Debilitating Symptoms by Middle Age
  Genetic Markers (CAG) Identify At-Risk Individuals
Brain Atrophy at Time of Death is Obvious and No Doubt Precedes Diagnosis
High-Risk Treatments (such as Implantable Drug Delivery Systems) Must be Weighed Against Likely Disease Progression

## Slide 24
Regional Brain Volume and White Matter Integrity Changes May Even Precede Clinical Symptoms
Accurate Detection Requires:
  Well Calibrated Acquisitions
  Robust Analysis Pipelines
    Registration
    Segmentation
    Diffusion Analysis

## Slide 25: TRACK-HD Stage 1 HD Subject
Baseline Scan

## Slide 26: TRACK-HD Stage 1 HD Subject
Year 1 Scan

## Slide 27: TRACK-HD Stage 1 HD Subject
BSI Overlay
Tissue loss
Tissue gain
Atrophy Rate: 1.9% Premanifest Rate: 0.7% Control Rate: 0.2%

## Slide 28: TRACK-HD Premanifest A Subject: voxel-compression mapping
Expansion ≥ 20%
Contraction ≤ 20%
12-month atrophy
24-month atrophy

## Slide 29: 24-month voxel-compression mapping
PreA
Control
HD2

## Slide 30
Change in WM vs controls (n=96)
HD2 (27)
HD1 (50)
PreHD-B (42)
PreHD-A (55)

## Slide 31: Summary
Medical Image Computing
  Powerful Tool Quantify Changes Due to Disease and Treatment
Careful Attention is Required
  Acquisition, Processing, and Interpretation
Resources
  Published Best Practices
  Freely Available Tools