## Slide 1: Some Aspects of Medical Image Registration
Marc Niethammer
CS/BRIC
February 20, 2014

## Slide 2: The sad reality: with a bit of hyperbole
State of Affairs
Image Registration
Registration works really well when there is not much to register!
Similar
images
Simple
transforms

However, in reality deformations are often more complex.
 Need for general deformable registration methods.

## Slide 3: Why is Deformable Image Registration Hard?
Motivation
Image Registration
Source Image
Target Image
?
Goal: Spatial alignment of two images (beyond affine).
minimize Irregularity of transformation + image mismatch

## Slide 4: Why is Deformable Image Registration Hard?
Motivation
Image Registration
Problem 1: Unsuitable deformation models
Image: classicwatersolutions.com
Does your brain, leg, heart, …
behave like a fluid?
Should it between two subjects?
Problem 2: Unsuitable similarity measures
What if images have
different appearances?
Problem 3: Unsuitable numerical solutions
Problem 4: How trustworthy is my solution?

## Slide 5: Why is Deformable Image Registration Hard?
Motivation
Image Registration
model complexity
model realism
model robustness
model realism
A: affine, NP: non-parametric (elastic, fluid, …)
Within subject (WS); between subject (BS); with pathology (P)
A-P
A-P
A-BS
A-BS
A-WS
A-WS
NP-P
NP-P
NP-BS
NP-BS
NP-WS
NP-WS

## Slide 6: What can be done about it?
Aim
Image Registration
Increasing robustness by
increasing model realism.
Decreasing complexity
while increasing realism.
Let’s look at some examples next …
model complexity
model realism
model robustness
model realism
NP-P
NP-P
NP-BS
NP-BS
NP-WS
NP-WS

## Slide 7
Similarity Measures

## Slide 8: Standard Similarity Measures
Overview
Similarity Measures
Standard similarity measures
  SSD
  Normalized cross correlation
  Mutual information
Fail if there is no clear correspondence (pathologies)
Not problem-specific
Do typically not exploit population or longitudinal information
May overall be too restrictive!

## Slide 9: Registration for Correlative Microscopy
Correlative Microscopy
Similarity Measures
Registration is hard if landmarks are not available
B
A’
Possible solution: Image Analogies (from graphics)
?

## Slide 10: Registration for Microscopy: Image Analogies
Correlative Microscopy
Similarity Measures
Solution approach:
Image Analogies:
A’ relates to B’
A’ relates to B’
unknown
learned
A
B’
B
A’

## Slide 11: Modelling of Appearance Changes
Contrast Inversion
Similarity Measures
Normal brain development (macaque)
Locally changing image intensities cause problems for
image similarity measures (SSD, mutual information, …)

## Slide 12: Modeling of Appearance Changes
Contrast Inversion
Similarity Measures
Normal temporal change (for a macaque monkey)
Proposed registration method
imposes a simple logistic model locally.
Exploits longitudinal information.

## Slide 13: Beyond Classical Similarity Measures
Overview
Similarity Measures
Problem-specific similarity measures
  Can learn mapping between modalities
  Can use longitudinal information
  Can use population information to be robust with respect to pathologies
Chances are that for complex models this will still not work.
Interactivity as discussed yesterday could be a good option.
Most straightforward models for similarity measures:
  Add landmark constraints
  Cost-function masking

## Slide 14: Fancy Cost-Function Masking
Geometric Metamorphosis
Similarity Measures
Developed method estimating two deformations, capturing
global brain deformations and local changes in appearance.
Traumatic brain injury
(real data)
Brain tumor
(simulated data)

## Slide 15: Composition of two deformations
Geometric Metamorphosis
Similarity Measures
Global background
deformation
Change of
geometric model
image
mask
matched to
matched to

## Slide 16: Image Composition
Geometric Metamorphosis
Similarity Measures
Growing
Shrinking
Image area gets “consumed”
cannot be used for matching
Image area gets “exposed”
cannot be used for matching
Image composition model
Notes: Image similarity maybe on a separate slide. (Check for time.)
Subheader for image similarity. Color code growing and shrinking with T_2 and I^\tau(1).
Say that image composition artificially creates 1-1 correspondence.

## Slide 17: Image Similarity
Our Solution Approach
Geometric Metamorphosis
Image composition model
alignment of corresponding image regions
alignment of
masks
Use your favorite similarity measure (CC,MI,SSD,…)

## Slide 18: Image Similarity
Overview
Similarity Measures
This is probably too complex a model in practice.
Standard cost-function masking may suffice.
Research question: “Can you discover regions that should
be masked by performing an initial faulty registration, fixing it by manual corrections and then determining what in the similarity measure tries to move the result away from the desired registration.”
Seems to have a flavor of sensitivity analysis.

## Slide 19
Deformation Models

## Slide 20: Standard Deformation Models
Overview
Deformation Models
Standard deformation models
  Parametric (rigid, affine, b-spline)
  Non-parametric: elastic, fluid, etc.
Assume globally valid transformation model.
Potentially good enough for some applications, but certainly not 100% realistic.
May overall be too simplistic!

## Slide 21: Deformation Model: Sliding
Sliding
Deformation Models
Problem: Standard non-parametric registration methods enforce unrealistic global smoothness.
Developed method based on anisotropic regularization,
specifically modeling for improved registration realism.
Joint work with Danielle Pace and Stephen Aylward.

## Slide 22: Locally-adaptive Regularization
Sliding
Deformation Models
Intra-organ smoothing
Smooth along tangential direction
Inter-organ coupling
Smooth normal components along normal direction
Sliding
Discontinuities in tangential components along normal direction
Diffusion tensors

## Slide 23: Deformation Model: LDDMM
LDDMM
Deformation Models
Large Displacement Diffeomorphic Metric Mapping (LDDMM)
?
Goal: Estimate optimal spatio-temporal velocity field to flow
one image into the other.
Optimal control
problem.
Hard problem: Millions of unknowns  need gradient!

## Slide 24: Deformation Model: LDDMM
LDDMM
Deformation Models
Large Displacement Diffeomorphic Metric Mapping (LDDMM)
?
Optimal control formulation (=constrained optimization)  opens possibility for more realistic models This is what most people in the field do now!
Constrained optimization
greatly simplifies the
derivation of optimality
conditions!

## Slide 25: Deformation Model: LDDMM
LDDMM
Image Registration
Large Displacement Diffeomorphic Metric Mapping (LDDMM)
?
Constrained optimization
greatly simplifies the
derivation of optimality
conditions!
This is probably one of the most complex registration formulations. But interesting for mathematical properties and also as a model problem for more sophisticated data-assimilation approaches.

## Slide 26: Longitudinal Data: Within and Between Subjects
Image-to-Image Registration
Overview
Deformation Models
?
Time-Series Modeling
Spline Models
Geodesic Regression

## Slide 27: Piece-wise linear vs. piece-wise geodesic
Piece-wise geodesic approach
Deformation Models
Piecewise Linear (Piecewise LDDMM-Geodesic for Images)
Problem: Not a generative model, possible over-fitting.
“Less flexible models” are likely much more realistic here.

## Slide 28: Dealing with Longitudinal Data: the Scalar Case
Linear Regression
Deformation Models
Linear Regression
Population Mean
Multiple linear regressions
“Average of linear regressions”
average

## Slide 29: Dealing with Longitudinal Data
Overview
Deformation Models
How to formulate the regression problem with images?
Geodesic Regression
Transport
Want a generative model
Want to change spaces
(e.g., atlas or other subject)

## Slide 30: Geodesic Regression
Geodesic Regression
Deformation Models
Linear regression can be formulated as an
optimal control problem with 2nd order dynamics.

## Slide 31: Linear Regression as a Dynamical System
Geodesic Regression
Deformation Models
Explicit model
Dynamic
formulation

## Slide 32: Linear Regression as a Dynamical System
Geodesic Regression
Deformation Models
Initial point free:
y-intercept
slope

## Slide 33: Transitioning to more Complex Data
Geodesic Regression
Deformation Models
1) Requires an initial value formulation of the registration:
State equation
Initial conditions
What is the equivalent to the 2nd order model?
2) Requires a measure of distance:
3) Requires a gradient with respect to the initial conditions
What is the equivalent to ?
How to compute for more complex system?
We can do this for images, diffeomorphisms, or also linear dynamical systems!

## Slide 34: Transitioning to the Image-Valued Case
Geodesic Regression
Deformation Models
1) Requires an initial value formulation of the registration:
Shooting equations (describing a geodesic)
LDDMM energy
(optimal control formulation)
LDDMM optimality conditions
(i.e., gradient = 0)
KKT conditions (constrained optimization)
This is a line!
Joint work with F. X. Vialard

## Slide 35: Transitioning to the Image-Valued Case
Geodesic Regression
Deformation Models
1) Requires an initial value formulation of the registration:
Shooting equations (describing a geodesic)
LDDMM energy
(optimal control formulation)
LDDMM optimality conditions
(i.e., gradient = 0)
KKT conditions (constrained optimization)
This describes a geodesic!

## Slide 36: Transitioning to the Image-Valued Case
Geodesic Regression
Deformation Models
2) Requires a measure of distance:
L2 distance or defined also by registration.
These are the
required distances

## Slide 37: Transitioning to the Image-Valued Case
Geodesic Regression
Deformation Models
3) Requires a gradient with respect to the initial conditions
Gradient ≈ initial conditions of adjoint to geodesic equations:
Gradient ≈ adjoint
for t=0.
What does this mean?
Intuitively: Allows computation of how initial conditions should change with respect to final conditions.

## Slide 38: Transitioning to the Image-Valued Case
LDDMM energy
(optimal control formulation)
LDDMM optimality conditions
(i.e., gradient = 0)
KKT conditions (constrained optimization)
Geodesic Regression
Deformation Models
3) Requires a gradient with respect to the initial conditions
Optimality conditions
of the optimality conditions
KKT conditions (constrained optimization)
Shooting equations
Shooting and
adjoint equations

## Slide 39: Shooting Example
Shooting
Deformation Models
“Happiness by registration”
The full transformation is encoded by the initial conditions!

## Slide 40: Shooting Example
Shooting
Deformation Models
“Happiness extrapolated”
This allows for extrapolation.

## Slide 41: Geodesic Regression: True Longitudinal Data
Geodesic Regression
Deformation Models
For small changes,
geodesic regression achieves
a good approximation.
Unregistered
GR

## Slide 42: Shortcomings of Geodesic Regression
Simplified Geodesic Regression
Deformation Models
Recall what we achieved so far:
Reformulation of least-squares
as a dynamical system
allowed extension to image-valued case.
Disadvantages:
  requires numerical solution
  requires in principle registration for residuals (unless analytical solutions are known)
  COSTLY

## Slide 43: Reinterpretation of Geodesic Regression
Simplified Geodesic Regression
Deformation Models
Can we find a simplified (approximate) geodesic regression?
Can we find yet another reformulation of LS?

## Slide 44: Reinterpretation of Geodesic Regression
Simplified Geodesic Regression
Deformation Models
Assume we know a point on the regression line

## Slide 45: Reinterpretation of Geodesic Regression
Simplified Geodesic Regression
Deformation Models
We can compute the slope of the regression line …
by appropriately averaging the slopes wrt. the base point

## Slide 46: Simplified Geodesic Regression
Simplified Geodesic Regression
Deformation Models
We can compute the slope of the regression line …
by appropriately averaging the slopes wrt. the base point
The slope is
which can be computed wrt. any
base point

## Slide 47: Approximation
Simplified Geodesic Regression
Deformation Models
Can do the same for images.
Results in simple averaging
of initial momenta
(=the Lagrangian multipliers)
Approximation allows for efficient computation of the
regression solution approximating geodesic distances.

## Slide 48: Synthetic Example
Simplified Geodesic Regression
Deformation Models
This can also be done with metamorphosis …
Time-series
Regression
result

## Slide 49: Deformation + Appearance: Metamorphosis
Metamorphosis
Deformation Models
?
Standard Image Registration
Assumes 1-1 correspondence
Image Metamorphosis
Registration and blending
…

## Slide 50: Texture Metamorphosis
Metamorphosis
Deformation Models
Allows for nice simultaneous warping and blending
Can be used for texture blending
Developed optimal-control-based numerical methods.
 Shooting method.
Time-series formulation.
Towards more realistic registrations w/ appearance change.

## Slide 51: Time-series Formulation
Metamorphic Geodesic Regression
Deformation Models
Same approximate way as before: average initial momenta
image
time series
shooting
result
momenta
Shooting now captures spatial and intensity changes. Example?

## Slide 52: Example toy result (to demonstrate feasibility)
Metamorphic Geodesic Regression
Deformation Models
simplified
geodesic
regression
simplified
metamorphic
geodesic
regression
Demonstrated feasibility of metamorphic regression solutions.
 Model likely too simplistic; more realistic models feasible.
young
old

## Slide 53
Uncertainty Estimation

## Slide 54: Motivation for Image Segmentation
Motivation
Uncertainty Quantification
Motivation: Image segmentation methods typically do not address segmentation uncertainty.

## Slide 55: Motivation for Image Segmentation
Motivation
Uncertainty Quantification
Motivation: Image segmentation methods typically do not address segmentation uncertainty.
How much can I trust my segmentation? Unclear!

## Slide 56: Motivation for Image Registration
Motivation
Uncertainty Quantification
Motivation: Image registration methods typically do not address segmentation uncertainty.

## Slide 57: Motivation for Image Registration
Motivation
Uncertainty Quantification
Motivation: Image registration methods typically do not address segmentation uncertainty.
How much can I trust my registration? Unclear!

## Slide 58: Motivation for General Image Analysis Problem
Motivation
Uncertainty Quantification
Depth
Cross-sectional area 
All processing steps have uncertainties.
How should we deal with those? Unclear!

## Slide 59: General
Motivation
Uncertainty Quantification
Quantifying uncertainty is very important.
While there is some work in this area, I would say that
overall it is greatly neglected …
Great opportunity to do something about it!

## Slide 60: Some Future Research Directions
What else there is to do
Future Directions
Image: wikipedia
Towards more realistic deformation models
  Appearance Changes / Pathologies / Development
  Learning from Limited Data
Time-Series and Longitudinal Data
  Higher Order Models
  Transport
  Dynamic Imaging
Uncertainty Estimation
  Registration & Segmentation
Multimodal Imaging
  Learning of Similarities

## Slide 61: Questions
Questions
Questions
Questions?