SPATIAL REGULARIZATION FOR fMRI DETECTION

Ron Kikinis, M.D.

Surgical Planning Laboratory

Brigham and Women’s Hospital

75 Francis Street

Boston, MA 02115

Voice: 1-617-732-7389

Fax: 1-617-582-6033

Email: kikinis@bwh.harvard.edu

Keywords: Functional MRI, Markov Random Fields, Spatial Regularization

SPATIAL REGULARIZATION FOR fMRI DETECTION

*¥Kikinis Ron, †Ou Wanmei, †Golland Polina, ¥†Wells William III,

¥Richter Carsten, ¥Liu Haiying, ¥Plesniak Wendy

†MIT Computer Science and Artificial Intelligence Laboratory, Cambridge MA

¥Surgical Planning Laboratory, Brigham and Women’s Hospital, Boston MA

We have developed a method for brain activation detection that employs Markov Random Fields (MRF) as spatial smoothing priors necessary due to the low signal-to-noise ratio of the fMRI signal. Furthermore, we extended the MRF prior to include anatomical information. The

anatomical prior, in the form of a segmented MRI scan, biases the activation detection towards the gray matter and inhibits smoothing of the activation maps across tissue boundaries. We have validated the method on a set of digital phantoms and a set of fMRI scans.

We are currently translating this work into 3D Slicer, an open source medical image analysis and visualization package developed and supported by Core2 activity, and are exposing the functionality through Slicer’s fMRIEngine module. The fMRIEngine module is designed to provide a framework for an extensible suite of activation detection algorithms; it currently provides a General Linear Model-based approach with which the MRF and anatomical priors can be used. Algorithms have been implemented in C++ as extensions to Kitware’s Visualization Toolkit (VTK) classes. A graphical user interface has been developed which allows a user to select a parametric map of activation from within the fMRI analysis workflow, to (optionally) load a segmented MRI scan and configure anatomical prior probabilities, to choose and configure a method for density estimation, and to configure the Meanfield approximation. Resulting color-coded posterior probabilities of brain activation can be viewed in Slicer’s 3D viewer and compared to original parametric brain activation map.

This prototype has been tested on the same datasets as used to validate the algorithms originally and has produced identical results. It is currently available to the wider community in the Slicer2.6 CVS repository but is not yet distributed with the Slicer2.6 release as refinements to the embodiment are ongoing. Our plans include incorporating this processing into Slicer tutorials provided to the user community, releasing the software with Slicer2.7, moving the implementation from VTK to ITK, and releasing the code into the ITK library to make the method available to a broader community.

Publications:

Wanmei Ou, Polina Golland. From Spatial Regularization to Anatomical Priors in fMRI Analysis. In Proc. IPMI 2005: Information Processing in Medical Imaging, LNCS 3565:88-100, 2005.

Wanmei Ou. fMRI Detection with Spatial Regularization. MIT Master Thesis, May 2005.

Grant Support: NIH NIBIB NAMIC 1U54 EB005149, NIH/NCRR NAC P41 RR13218, NIH NINDS R01-NS051826.

email: kikinis@bwh.harvard.edu